## Slide 1
Soft Tissue Robotics
Introduction to User Materials in Abaqus FEA
Harnoor Saini
IRTG STR regular meeting 16.12.2019 Stuttgart, Germany

## Slide 2: Introduction
Finite Element Analysis
http://www.iue.tuwien.ac.at/phd/rovitto/node72.html
https://www.theseus-fe.com/simulation-software/heat-transfer-analysis
Heat-transfer
http://www.tam.northwestern.edu/tb/D26/
Structural mechanics
Electromagnetic
https://www.3ds.com/products-services/simulia/products/opera/
Maxwell equations
Momentum balance
Heat equation (Fourier)

## Slide 3: Introduction
Material Modelling
https://nptel.ac.in/courses/105106049/
1D Example

## Slide 4: Introduction
Abaqus/implicit uses information at current and previous time
Abaqus/explicit uses information only from previous time
User Materials in Abaqus (Explicit)
VUMAT
Abaqus/Explicit
https://nptel.ac.in/courses/105106049/

## Slide 5: VUMAT
Basic Structure
…
VUMAT
7
8
9
4
5
6
1
2
3
Per element; call VUMAT:

## Slide 6: VUMAT
subroutine vumat(
C Read only (unmodifiable)variables -
1 nblock, ndir, nshr, nstatev, nfieldv, nprops, lanneal,
2 stepTime, totalTime, dt, ...,
4 tempOld, stretchOld, defgradOld, fieldOld,
5 stressOld, ...,
C Write only (modifiable) variables -
7 stressNew, stateNew, enerInternNew, enerInelasNew )
C
include 'vaba_param.inc'
C
dimension props(nprops), density(nblock), coordMp(nblock,*),
1 charLength(nblock), strainInc(nblock,ndir+nshr),
2 relSpinInc(nblock,nshr), tempOld(nblock),
3 stretchOld(nblock,ndir+nshr),
4 ...
2 enerInternNew(nblock), enerInelasNew(nblock),
do 100 km = 1,nblock
user coding
100 continue
return
end
Welcome to the real world
VUMAT
stretchNew(nblock)
stressOld(nblock,ndir+nshr)
props(nprops)
totalTime,...
stressNew(nblock,ndir+nshr)

## Slide 7: VUMAT
A worked example – three-dimensional isotropic, linear elasticity
https://www.ecourses.ou.edu/cgi-bin/eBook.cgi?doc=&topic=me&chap_sec=01.4&page=theory
Generalise 1D elasticity to 3D
Implement in FORTRAN according to VUMAT requirements
Validate against in-built Abaqus linear elasticity

## Slide 8: VUMAT
do i = 1,nblock
c sigma_11 component
stressNew(i,1)=
c sigma_22 component
stressNew(i,2)=
c sigma_33 component
stressNew(i,3)=
c sigma_12 component (shear stress)
stressNew(i,4)=
c sigma_13 component (shear stress)
stressNew(i,5)=
c sigma_23 component (shear stress)
stressNew(i,6)=
end do
A worked example – three-dimensional isotropic, linear elasticity
 Linear or non-linear analyses: (1) material (2) geometric (3) boundary conditions
reference configuration
current configuration

## Slide 10: Stable time increment